## Slide 1: External GPS setup for ArcPad on Mesa 2
14APR2016
Juniper Systems, Inc.

## Slide 2: From the Mesa 2 home screen access the Settings control panel

## Slide 3: Select “Devices”, where the bluetooth control panel is located

## Slide 4: Select “Bluetooth” to access the bluetooth control panel

## Slide 5: Slide the Bluetooth slider to “ON” to enable Bluetooth. Available devices will begin to appear in a list below

## Slide 6: Click on the “Arrow 100 xxx” or similar GPS bluetooth device, and click on “pair”. PC will display “connected”.

## Slide 7: Check the outgoing com port assigned to the BT GPS; this is the port that you will select in ArcPad. Close the Settings control panel

## Slide 8: Launch ArcPad. Select GPS Preferences.

## Slide 9: Select “NMEA 0183”, and select the com port for the connected bluetooth port. (baud rate setting not required for bluetooth connection). Press OK.

## Slide 10: Select GPS/Rangefinder Debug to confirm the connection works. NMEA data will display on the screen.

## Slide 11: Select GPS Position Window to confirm position data is being received.